## Slide 1: Payette: Overview
Payette
Payette is an object oriented material model driver written in Python designed for rapid development and testing of material models
MOTIVATION
Modern finite element codes are too complex and compile/link times too long for efficient material model development. Additionally, features such as artificial viscosity can mask the actual material response from constitutive model development. Single element drivers allow the constitutive model developer to concentrate on model development and not the finite element response.
HISTORY
Payette is an outgrowth of Tom Pucick’s MMD and Rebecca Brannon’s MED drivers. Both these other drivers are written in Fortran.

## Slide 2: Payette: Overview
APPROACH
Payette exercises the material model by “driving” it with the required mechanical and electrical inputs
MECHANICAL DRIVERS
  Direct
    Strain rate
    Strain
    Deformation Gradient
    Displacement
    Velocity
  Inverse
    Stress
    Stress rate
ELECTRICAL DRIVERS
  Direct
    Electric Field

## Slide 3: Payette: Building
SYSTEM REQUIREMENTS
  Python 2.6 or newer with Numpy, SciPy, SymPy, matplotlib
  Tested on Mac OSX 10.6, Linux RHEL 5, Linux Ubuntu
OBTAINING
  svn://lenny.eng.utah.edu/csm/local/svn/Payette/trunk
ENVIRONMENT SETUP
  Create environment variable PAYETTE_HOME that points to Payette/trunk
  Add $PAYETTE_HOME/Toolset to $PATH
KAYENTA MATERIAL MODEL
  Create environment variable PAYETTE_KAYENTA that points to src/ directory for Kayenta
BUILDING
  In $PAYETTE_HOME/Toolset, execute % python buildPayette
  %./rebuildPayette

## Slide 4: Payette: Running
RUNNING
  Interacting with Payette is through the runPayette script and properly formatted input files.
  Basic usage: % runPayette input_file
  For complete list of options for runPayette execute % runPayette –h for complete list of options
OUTPUT
  runPayette creates the following output for a simulation “simname”:
    simname.log – log file
    simname.props – list of checked properties
    simname.prf – restart file
    simname.out – output file
    simname.math1 – Mathematica auxiliary file
    simname.math2 – Mathematica auxiliary file

## Slide 5: Payette: Input File
INPUT BLOCKS
Interact with Payette through blocks:
begin <block type> [block title]
end <block type>
REQUIRED BLOCKS
    begin simulation <title>
    begin material
    constitutive model <model>
    [material options]
    end material
    begin boundary
    [boundary options]
    begin legs
    [leg options]
    end legs
    end boundary
    end simulation

## Slide 6: Payette: Material Block
MATERIAL BLOCK
    begin material
    constitutive model <model>
    parameter 1 <value>
    parameter 2, <value>
    .
    .
    .
    parameter n = <value>
    end material
EXAMPLE
    begin material
    constitutive model elastic
    bkmod = 130.E9
    shmod = 57.E9
    end material

## Slide 7: Payette: Boundary Block
BOUNDARY BLOCK
    begin boundary
    kappa = 0.
    ampl = 1.
    ratfac = 1.
    tstar = 1
    sstar = 1.
    estar = 1.
    fstar = 1.
    dstar = 1.
    efstar = 1.
    stepstar = 1.
    emit = all {all,sparse}
    screenout = false
    nprints = 0 [nsteps]
    begin legs
    [leg options]
    end legs
    end boundary
(Default values shown)

## Slide 8: Payette: Legs Block
LEGS BLOCK
    begin legs
    # leg no, time, nsteps, ltyp, c[ij]
    end legs
LTYP
No. | Description | Type | Dim
1 | Strain rate control | mech | 6
2 | Strain control | mech | 6
3 | Stress rate control | mech | 6
4 | Stress control | mech | 6
5 | Deformation gradient control | mech | 9
6 | Electric field control | elec | 3
7 | Electric displacement control | elec | 3
8 | Displacement control | mech | 3

## Slide 9: Payette: Boundary/Legs Block
EXAMPLE
    begin boundary
    kappa = 0.
    ampl = 10.
    sstar = 1.25
    begin legs
    # leg no, time, nsteps, ltyp, c[ij]
    0, 0., 0, 222222, 0., 0., 0., 0., 0., 0.
    1, 1., 1000, 444222, 1.e7, 0., 0., 0., 0., 0.
    end legs
    end boundary

## Slide 10: Payette: Optional Blocks
OPTIONAL BLOCKS
    begin mathplot
    VAR1 VAR2 VAR3
    var4, var5, var6,
    ...
    end mathplot
EXAMPLE
    begin mathplot
    time sig11 sig22 sig33
    eps11 eps22 eps33
    I1 ROOTJ2
    end mathplot

## Slide 11: Payette: Example Input File
begin simulation test elastic
begin boundary
kappa = 0
tstar = 1.
ampl = 1
begin legs
0, 0., 0., 222222, 0., 0., 0., 0., 0., 0.
1, 1., 1., 222222, .1, 0., 0., 0., 0., 0.
2, 2., 1., 222222, 0., 0., 0., 0., 0., 0.
3, 3., 1., 888, .10517091808, 0., 0.
4, 4., 1., 888, 0., 0., 0.
5, 5., 1., 555555555, 1.10517091808, 1.0, 1.0, 0., 0., 0., 0., 0., 0.
6, 6., 1., 555555555, 1.0, 1.0, 1.0, 0., 0., 0., 0., 0., 0.
end legs
end boundary
begin material
constitutive model elastic
RHO 1000
A1 23e6
G 53.e9
K 135.e9
end material
begin mathplot
sig11, sig22, sig33,
qssigxx
end mathplot
end simulation

## Slide 12: Payette: Testing
TESTING
  Testing Payette is through the testPayette script
  Basic usage: % testPayette
  For complete list of options for testPayette execute % testPayette –h for complete list of options
OUTPUT
  testPayette creates the following output in the directory executed TestResults.$OSTYPE/ summary.html summary.py
  Open TestResults.$OSTYPE/summary.html for a summary of tests run
EXAMPLE: Run “fast” kayenta tests on 4 processors
  % testPayette –k fast –k kayenta –j 4